## Slide 1
Chapter 8
— 例题与作业

## Slide 2: Examples
Paging中逻辑地址-物理地址-页表结构及地址变换
  例1. Fig. 8.9
  例2，例3，例4, 例5
  例6. EAT in TLB-based paging
Paging with segmentation
  例7，例8，例9
  多级页表结构
  例10 Fig. 8.12, 例11
  例12. 内存扩展-CPU利用率-吞吐量
  补充作业
作业：
8.3, 8.9, 8.12
补充作业

## Slide 3: 例1. 逻辑地址-物理地址变换
Fig.8.9
  page size 4 bytes
  Logical space
  4 pages =16 bytes=24 B
  logical address consists of m=4 bits, i.e. **, **
  Physical memory
  8 frames =32 bytes=25B
  physical address consists of 5 bits, i.e. ***, **
P# :
0
1
2
3
f#:
f# :
0
1
2
3
4
5
6
7
e.g. m=4, n=2

## Slide 4: 例1.
  Address mapping in Fig. 8.9
  e.g.1 logical address 0, i.e. 00,00
  page number=00, page offset=00
  page table: page 0 is allocated to frame 5, that is, 101
  physical address : 10100, or: 5 * 4 + 0 =20
  e.g.2 logical address 9, i.e. 10,01
  page number=2, i.e, 10, page offset=1, i.e. 01
  page table: page 2 is allocated to frame 1, that is, 001
  physical address : 1* 4 + 1 =5, or: 00101

## Slide 5: 例2
  On a system using fixed partitions with sizes 28, 224 and 264 bytes, how many bits must the limit register have?
  Answer
  64 bits in the limit register

## Slide 6: 例3
  On a simple (not virtual memory ) paging system with 224 bytes of physical memory, 256 pages of the logical address space, and a page size of 210 bytes, how many bits are in a logical address?
  Answer
  the logical address space contains 256 (＝28) pages of 210 bytes each, making the total logical address space 210 × 28 = 218 bytes
  an 18-bit address is required to cover a 218-byte address space
  note: the size of the logical address space is less than that of physical memory

## Slide 7: 例4
  On a simple paging system with a page table containing 512 entries of 16 bits (including one valid/invalid bit) each, and a page size of 1024 (i.e.210 ) bytes
  (a) what is the size of the logical address space?
    219 = the number of pages * the size of pages
  = 512*1024 (bytes)
  (b) how many bits are there in a logical address?
    19 = log2(the size of logical address space)
  = log2(512 * the size of pages)=log2(512*210) (bits)
  (c) how many bits in the physical address specify the frame number?
    15= the length of entries in the page table -1
  =16 -1 (bits)

## Slide 8
page number
18
10
page/frame offset
9
0
Logical Address Space
15 high bits of physical address
v
….
512
=29
entries
0
14
15
Page
Table
concatenate
10 low bits
15 high bits
Physical Address Space
frame#

## Slide 9: 例4
  (d) how many bits in the physical address specify the offset within the frame?
    10 = log2(the size of a frame) = log2(1024) (bits)
  (e ) what is the size of the physical address space ？
    225 bytes = the number of frames * the size of frames
  = 2(16-1) *210 bytes
  (f) how many bits are there in a physical address?
    25 = log2(the size of physical memory)
  = log2 (225 bytes ) bits

## Slide 10: 例5
  On a simple paging system with 232 bytes of physical memory, 212 pages of the logical address space, and page size of 512=29 bytes
  (a) how many bits are in a logical address?
    21 = log2(the size of logical address space)
  = log2(212 pages * page size ) = log2(212 * 29)
  (b) how many bytes are there in a frame?
    512 bytes, the same as that in a page
  (c) how many bits in the physical address specify the frame number?
    23 = log2(physical memory size232) – log2(page size)
  = log2(232) - log2(29)

## Slide 11: 例5
  (d) how many entries are in the page table (how long is the page table) ?
    212, the number of pages in the logical address space
  (e) how many bits in the logical address specify the page number?
    12 = log2(the number of pages) =log2(212)
  (f) how many bits in the logical address specify the offset within a page?
    9 = log2(the size of pages) =log2(29)

## Slide 12: 例6. EAT in TLB-based paging
  Hit ratio  – percentage of times that a page number is found in the TLB
  E.g. It is supposed
  the hit ratio is 80%
  it takes 20 ns to search the TLB and 100ns to access memory, then
  a mapped-memory access takes 120 ns when the page number is in TLB, because it takes 20ns to search TLB and 100 ns to access memory
  if the page number is not in TLB (20 ns), the we must first access the memory for the page table and frame number (100ns), then access the desired the page in memory (100ns), for a total 220 ns
  by weighting each case by its probability, we obtain the EAT as
  EAT = 0.80 ╳ (20+100) + 0.20 ╳ (20+ 100 + 100)
  = 140 ns

## Slide 13: 例7
  On a system of segmentation with paging, the logical address space consists of up to 16 segments where each segment can be up to 216 bytes long. The hardware pages each segment into 512-byte pages
  how many bits in the logical address specify the following ?
  (a) segment number
    4 = log2 (the number of segments)= log2(16)
  (b) page number
    7 = log2(the number of pages)
  = log2(the size of segments /
  the size of pages )
  = log2( 216 /29)
segment
number
offset in segment
page
number
offset
in page

## Slide 14: 例7
  (c) offset within pages
    9 = log2(the size of pages) = log2 512
  (d) entire logical address
    20 = the bits for segment number
  + the bits for page number
  + the bits for offset within pages
  or: 20 = log2(the size of the logical address space)
  = log2(the number of segments * the size of segments)
  = log2(16 * 216 )
segment
number
offset in segment
page
number
offset
in page

## Slide 15: 例8
  Consider a system using segmentation with paging management scheme, whose physical memory is of 235 bytes. The logical address space consists of up to 8 segments. Each segment can be up to 213 pages, and the page size of 512 bytes,
  (1) How many bits are there in the entire logical address?
    the entire logical address consists of segmentation and offset in segmentation, and offset in segmentation is divided into page number and page offset, so entire logical address has
  log2 (8) + log2(213) + log2 (512) = 3 + 13 +9 =25 bits

## Slide 16: 例8
  (2) How many bits in the logical address specify the page number?
    each segment consists of up to 213 pages, so log2(213) = 13 bits in the logical address specify the page number
  (3) What is the size of a frame?
    the size of a frame is equal to that of a page, i.e. 512 bytes
  (4) How many bits in the physical address specify the frame number?
    the total size of physical memory is 235 bytes, and each frame is 29 = 512 bytes, so there are 26 = (35 – 9) bits in the physical address specify the frame number

## Slide 17: 例8
  (5) How many bits in the physical address specify the frame offset?
    the number of bits in the physical address specifying the frame offset depends on the size of the frame, so
  log2 (29) = 9 bits
  in the physical address specify the frame offset
  (6) How many entries are there in the page table for each segmentation, i.e. how long is the page table for each segmentation?
    each entry in the page table corresponds to a page in the segment, each segment can be up to 213 pages, so there are 213 entries in the page table for each segment

## Slide 18: 例9
  A system using segmentation with paging has a 16-bit logical address space with 2 segments per process and a page size of 212 bytes
  (1) Draw a figure to indicate the components of a logical address, and specify how many bits are there in each component

## Slide 19: 例9
  (2) If the content of the segment and page tables is specified below (all values binary).
For the following binary logical addresses, indicate what physical address they would be translated into, or if they would a page fault.
(a) 0, 001, 010001010111
(b) 0,100, 010011111111
(c) 1, 011, 010011000111
(d) 1, 110, 001011000111

## Slide 20
(a) 0 001 010001010111 ==> 011101, 010001010111
(b) 0 100 010011111111 ==> 111010, 0100 1111 1111
(c) 1 011 010011000111 ==> 011001, 010011000111
(d) 1 110 001011000111 ==> page fault
(2) answers
4页
5页
#Page
000
001
010
011
100
101
110
111
P#
000
001
010
011
100
101
110
111

## Slide 21: 例10 Fig. 8.12
  A logical address (on 32-bit machine with 4K page size) is divided into:
  a page number consisting of 20 bits
  a page offset consisting of 12 bits
  The page table itself is also paged, the page number is further divided into
  a 10-bit page number,
  a 10-bit page offset.
注：高位一分为二，各10bits，
内外页表采用相同大小的chunk
page offset
pi
d
10
10
12
page number
p2
outer page
inner page
the number of entries in the table: 220=1M=210*210=1K*1K
1M=220 entries in the page table is divided into 210 chunks, and each chunk contains 210 entries and located in a contiguous space

## Slide 22: Fig.8.12. Two-level page-table scheme
220=1M entries,
210*4 bytes in size
210=1K entries
210=1K entries
220*4K
=4 GB
chunk0
chunk1
chunk210
The page table occupies (1+210) chunks, (1+210) *210*4 =(4K + 4M) Bytes
注：内外页表采用相同大小的chunk

## Slide 23: Fig.8.13 Address-translation scheme for a two-level 32-bit paging architecture

## Slide 24
页目录地址
目录位移
页表位移
页位移
虚拟地址
页表地址
.
.
.
页目录(每进程一个)
块号
.
.
.
页表
代码或数据
.
.
.
内存块
二级页表结构及地址映射
+
+

## Slide 25: 例11
  某计算机采用two-level paging的分页管理机制，按字节编址，页大小为210bytes，页表项大小为2字节，逻辑地址结构为
  逻辑地址空间大小为216pages
  问：表示整个逻辑地址空间的页目录表中包含表项个数至少是：B
A. 64 B. 128 C. 256 D. 512
页目编号/outer page | 页号/inner page | 页内偏移/offset

## Slide 26: 例11
  页大小为210bytes，页表项大小为2字节，
  逻辑地址空间大小为216pages，共210*216bytes=226bytes, 逻辑地址26bits
  假设：内页表中多个chunk、外页表的1个chunk均采用1个page大小（210bytes ）的内存块来存储页表项，而1个页表项占2个字节，故
  一个chunk中可以存储210/2=512=29个页表项，所以逻辑地址中内页号所占的地址位数为9位。由此推出，外页所占位数为7位，外页有128个表项；
  共有216个pages，一个内页表chunk可以存储512个page的物理地址/frame首地址高位，需要216 /512= 27 =128个内页表chunk，故外页表中应有128个表项指向内页中的每个chunk。
页目编号/outer page | 页号/inner page | 页内偏移/offset
0
25
10 9
18

## Slide 27: 例12 内存扩展-CPU利用率-吞吐量
  1个多道程序设计系统采用实存管理技术并发执行多个大小均为300K的程序。假设各个进程在执行过程中有80%的I/O等待时间（即进程等待I/O的时间占其生命周期时长的80%）
  (1) 当系统内存为900K时，有多大比例的cpu时间被浪费掉了？cpu利用率是多少？为什么?
  (2) 若再增加300K内存，cpu利用率可提高多少？
  (3) 假设系统内每个进程在其生命周期内处于running态执行程序指令的总时间均相同。当系统内存由900K增至1200K时，系统吞吐量可提高多少

## Slide 28: 例12 内存扩展-CPU利用率-吞吐量
  (1) 当系统内存为900K时, 系统可容纳3个进程同时并发执行
  根据题意，进程在执行过程中有80%的I/O等待时间, 表明进程等待I/O的时间占其生命周期时长的80%, 进程处于waiting状态的概率为0.8
  对系统内并发执行的n个进程, 当这n个进程同时处于I/O等待时, cpu是空闲的
  系统内3个并发进程同时处于I/O等待态而导致CPU空闲的概率为(80%)3=0.512
  因此，系统有51.2%的CPU时间被浪费掉了，系统CPU的利用率为(1—51.2%)＝48.8%。

## Slide 29
CPU burst
20%
I/O burst
80%
CPU burst
20%
I/O burst
80%
CPU burst
20%
I/O burst
80%
P1, P2, P3 blocked
CPU空闲
51.2%
P1
P2
P3

## Slide 30: 例12 内存扩展-CPU利用率-吞吐量
  (2) 若再增加300K内存，系统可容纳４个进程同时并发执行
  此时，CPU的利用率为 (1— (80%)4) = (1— 0.4096) = 0.5904
  所以，若再增加300K内存，cpu利用率可提高：
(0.5904—0.488) / 0.488 = 20.98%

## Slide 31: 例12 内存扩展-CPU利用率-吞吐量
  (3)根据题意，设系统内每个进程在其生命周期内处于running态执行程序指令(CPU burst)的总时间均为T
  当系统内存为900K时, 系统可容纳3个进程并发执行。如果3个进程全部并发执行完所需时间为L3，则：
CPU的利用率=3T / L3=48.8%,
L3 = 3T / (48.8%),
, 系统吞吐量Th3=3/ L3= (48.8%) / T

## Slide 32: 例12 内存扩展-CPU利用率-吞吐量
  当系统内存由900K增至1200K时，系统可容纳４个进程同时并发执行。设4个进程全部并发执行完所需时间为L4，则:
CPU的利用率 = 4T / L4=59.04%,
L4=4T / (59.04%),
系统吞吐量Th4=4/ L4= (59.04%) / T
  因此，若再增加300K内存，系统吞吐量可提高：
［(59.04%) / T —(48.8%) / T］/ [(48.8%) / T]
= (0.5904—0.488) / 0.488 = 20.98%
= 20.98%
CPU利用率提高系统吞吐量提高

## Slide 33: 补充作业
  On a simple paging system with a page table containing 1024 entries of 13 bits (including one valid/invalid bit) each, and a page size of 4096 bytes
  （a) what is the size of the logical address space?
  (b) how many bits are there in a logical address?
  (c) how many bits in the physical address specify the frame number?
  (d) how many bits in the physical address specify the offset within the frame?
  (e ) what is the size of the physical address space ？
  (f) how many bits are there in a physical address?
要求：参照例4，画图